## Slide 1: Course: Thermofluids ( MEC235)
Prepared By: Sudhanshu Dogra
Assistant Professor/COD(Thermal Engineering)
UID: 16900
School of Mechanical Engineering
Lovely Professional University

## Slide 2: Carnot cycle
The cycle was first suggested by a French engineer Sadi Carnot in 1824 which works on reversible cycle and is known as Carnot cycle.
Any fluid may be used to operate the Carnot cycle which is performed in an engine cylinder the head of which is supposed alternatively to be perfect conductor or a perfect insulator of a heat. Heat is caused to flow into the cylinder by the application of high temperature energy source to the cylinder head during expansion, and to flow from the cylinder by the application of a lower temperature energy source to the head during compression.

## Slide 3: Assumptions
The assumptions made for describing the working of the Carnot engine are as follows :
(i) The piston moving in a cylinder does not develop any friction during motion.
(ii) The walls of piston and cylinder are considered as perfect insulators of heat.
(iii) The cylinder head is so arranged that it can be a perfect heat conductor or perfect heat insulator.
(iv) The transfer of heat does not affect the temperature of source or sink.
(v) Working medium is a perfect gas and has constant specific heat.
(vi) Compression and expansion are reversible.

## Slide 4: Processes in Carnot Cycle
1) Reversible Isothermal process (1-2): in which Q1 heat enters the system at t1 reversibly from a constant temperature source at t1 whe the cylinder is in contact with diathermic cover. The Internal energy of the system increases.
From 1st law: Q = ∆U + W
Q1-2 = U2 – U1 + W1-2 (1)

## Slide 5: Contd…
2) Reversible Adiabatic process(2-3): in which diathermic cover is replaced with adiabatic cover and work is done by the system due to expansion. Temperature of the system decreases from t1 to t2.
From 1st law: Q = ∆U + W
Q2-3 = U3 – U2 + W2-3
0 = U3 – U2 + W2-3 (2)

## Slide 6: Contd…
3) Reversible Isothermal process (3-4): in which Q2 heat leaves the system reversibly to a constant temperature sink at t2 whe the cylinder is in contact with diathermic cover. The Internal energy of the system decreases.
From 1st law: Q = ∆U + W
Q3-4 = U4 – U3 + W3-4 (3)

## Slide 7: Contd…
4) Reversible Adiabatic process(4-1): in which diathermic cover is replaced with adiabatic cover and work is done on the system due to compression. Temperature of the system increases from t2 to t1.
From 1st law: Q = ∆U + W
Q4-1 = U1 – U4 + W4-1
0 = U3 – U2 + W4-1 (4)

## Slide 8: Contd…
The equations are:
Q1-2 = U2 – U1 + W1-2 (1)
0 = U3 – U2 + W2-3 (2)
Q3-4 = U4 – U3 + W3-4 (3)
0 = U3 – U2 + W4-1 (4)
Adding all the above equations, we get:
Q1-2 + 0 + Q3-4 + 0 = U2 – U1 + W1-2 + U3 – U2 + W2-3 + U4 – U3 + W3-4 + U3 – U2 + W4-1
Q1-2 + Q3-4 = W1-2 + W2-3 + W3-4 + W4-1 (First law of Thermodynamics for a Cyclic process)

## Slide 9: Carnot Theorem
“It states that of all engines operating between a given constant temperature source and a given constant temperature sink, none has a higher efficiency than a reversible engine”.
HEA and HEB are the two engines operating
between the given source at temperature T1
and the given sink at temperature T2.
Let HEA be any heat engine and HEB be any
reversible heat engine. We have to prove that
efficiency of HEB is more than that of HEA.
Let us assume that ηA > ηB.

## Slide 10: Contd…
Let the rates of working of the engines be such that

## Slide 11: Contd…
Now, let HEB be reversed. Since HEB is a reversible heat engine, the magnitudes of heat and work transfer quantities will remain the same, but their directions will be reversed. Since WA > WB, some part of WA (equal to WB) may be fed to drive the reversed heat engine ∃HB. Since Q1A = Q1B = Q1, the heat discharged by ∃HB may be supplied to HEA. The source may, therefore, be eliminated. The net result is that HEA and ∃HB together constitute a heat engine which, operating in a cycle produces net work WA – WB while exchanging heat with a single reservoir at T2. This violates the Kelvin-Planck statement of the second law. Hence the assumption that ηA > ηB is wrong. Hence, ηB > ηA .

## Slide 12: Entropy

## Slide 13: Clausius inequality

## Slide 14: Available energy

## Slide 15: Third law of Thermodynamics

## Slide 16: Entropy of Isolated system

## Slide 17
THANKS